Program name (with extension): BentSim.scad
Target language digram: fr

With this text, comes a translation macro for OpenSCAD customizer.
You shall select the appropriate text file before starting the macro (OpenSCAD_translate).
As for now, it is very primitive and don’t really ‘detect’ a langage.

It does have very simple actions and now is not capable to handle more than the main langage and another one. That may not be very big work to modify the macro to handle multiple languages, anyway:

Input fields description
When encountering a comment with the langage prefix (defined in a macro variable), it remove the next line (supposedly the default langage). The prefix of the comment line is also removed so:
//lg:Localized field description
//Field original description
myfield=0; // [0:2:10]
will became:
//Localized field description
myfield=0; // [0:2:10]

For tabs (note that tabs with no contents are not displayed), the following
/*lg:[Localized tab]*/
/*[Default tab]*/
will became:
/*[Localized tab]*/

and when variables use localized names, the translation shall be AFTER and commented – to not became a description-
name = "Peter"; // ["Peter", "John", "Edward"]
//fr::name = "Pierre"; //["Pierre", "Jean", "Edouard"]
will became (original line removed and next line uncommented):
name = "Pierre"; //["Pierre", "Jean", "Edouard"]

To be usable, you will need to define in a [Hidden] tab something like that
ar_name = ["Peter", "John", "Edward"];
//lg::ar_name = ["Pierre", "Jean", "Edouard"];
To be used with something like that:
if (name==ar_name[i]) {do something}

Original english comments to be removed (if there is an equivalent in local langage)
/*en+
this is a multiline comment
for test
*/
the last line shall only have two char comment closing (whole line will be removed)
Local langage comment will look like:
/*fr+
Ceci est un commentaire
multiligne à fin de test
*/

Important note:
  All comments shall start at the beginning of a new line to be interpreted by the macro, without space	.